# PIRA 200
Astronomy

| Orrery Phases of the Moon | Retrograde Motion Model Celestial Sphere Sunspots on the Overhead | Random Walk Expanding Universe Membrane Table / Black Hole |
| --- | --- | --- |

| ASTRONOMY AND ASTROPHYSICS | 8A10.10 | PLANETARY ASTRONOMY |
| --- | --- | --- |
| Solar System Mechanics |
| Orrery |
|  | The system is not to scale. The periods of the orbit are scaled. All the planets are on friction clutches and can be positioned by hand. Workshop Video |

| ASTRONOMY AND ASTROPHYSICS | 8A10.25 | PLANETARY ASTRONOMY |
| --- | --- | --- |
| Solar System Mechanics |
| Phases of the Moon |
|  | Rotate the camera in a complete circle keeping the Moon globe, or the cork ball used as the Moon, in the light. Workshop Video |

| ASTRONOMY AND ASTROPHYSICS | 8A10.55 | PLANETARY ASTRONOMY |
| --- | --- | --- |
| Solar System Mechanics |
| Retrograde Motion Model |
|  | Use the crank on the back to move the two planets around the sun. A sliding rod shows the relative motion of the two planets. |

| ASTRONOMY AND ASTROPHYSICS | 8A10.80 | PLANETARY ASTRONOMY |
| --- | --- | --- |
| Solar System Mechanics |
| Celestial Sphere |
|  | No instructions |

| ASTRONOMY AND ASTROPHYSICS | 8B10.30 | STELLAR ASTRONOMY |
| --- | --- | --- |
| Misc. |
| Sunspots on the Overhead |
|  | A light bulb on a variac is turned up to visible glow and placed on an overhead projector that is turned off. When the overhead is turned on, the filament appears as a dark spot. Workshop Video |

| ASTRONOMY AND ASTROPHYSICS | 8B10.35 | STELLAR ASTRONOMY |
| --- | --- | --- |
| Misc. |
| Random Walk |
|  | Use a Bumble Ball ( a common toy ) to illustrate the random walk of high energy photons in a star. Workshop Video |

| ASTRONOMY AND ASTROPHYSICS | 8C10.10 | COSMOLOGY |
| --- | --- | --- |
| Models of the Universe |
| Expanding Universe |
|  | Five 10cm Styrofoam balls are threaded onto a rubber hose at equal intervals. Pull on the free end and watch the expanding intervals. Workshop Video |

| ASTRONOMY AND ASTROPHYSICS | 8C20.20 | COSMOLOGY |
| --- | --- | --- |
| Models of the Universe |
| Membrane Table / Black Hole |
|  | Swimsuit fabric stretched over a wood frame is deformed with a weight and balls are rolled around. Workshop Video |