# PIRA 200
Modern Physics

| Discharging Zinc Plate Vibrating Circular Wire | Electron Diffraction Student Gratings and Line Sources | Geiger Counter and Samples Diffusion Cloud Chamber Lorentz Transformation / Time Dilation |
| --- | --- | --- |

| MODERN PHYSICS | 7A10.10 | QUANTUM EFFECTS |
| --- | --- | --- |
| Photoelectric Effect |
| Discharging Zinc Plate |
|  | A polished zinc plate sits atop an electroscope. Charge the electroscope with a rod. Turn on the UV light. Removed the protective glass plate to expose the zinc plate to the UV rays. Replace the glass plate. Do not turn the UV light towards the students. Workshop Video |

| MODERN PHYSICS | 7A50.40 | QUANTUM EFFECTS |
| --- | --- | --- |
| Wave Mechanics |
| Vibrating Circular Wire |
|  | The PASCO signal generator drives the PASCO mechanical vibrator. The three node resonance is at 20Hz. Turn up the amplitude after finding the resonance. Other resonances are at 60, 100, 140 Hz. Pin the wire at 180 degrees from the mechanical vibrator to get full numbers of waves. Workshop Video |

| MODERN PHYSICS | 7A60.10 | QUANTUM EFFECTS |
| --- | --- | --- |
| X-ray and Electron Diffraction |
| Electron Diffraction |
|  | Rings or spots diffraction patterns can be shown to the class using a TV camera. The beam and potential will already be adjusted. Turn up the bias until the pattern appears. Do not let the current exceed 30 microamps. Turn down the bias when you are done. |

| MODERN PHYSICS | 7B10.10 | ATOMIC PHYSICS |
| --- | --- | --- |
| Spectra |
| Student Gratings and Line Sources |
|  | Pass out the 1"x1" gratings to the students. These have 13,400 lines per inch. Turn on one of the light sources. There is a single filament white light source and six discharge tubes, H, He, Kr, Ar, O2 and Ne. Caution: Turn off the power on the carousel before turning to the next discharge tube. Workshop Video |

| MODERN PHYSICS | 7D10.10 | NUCLEAR PHYSICS |
| --- | --- | --- |
| Radioactivity |
| Geiger Counter and Samples |
|  | Turn on the counter and place sample under Geiger Tube. Test to see how distance from the sample affects the count. Place objects like: paper, wood, lead and other items between the source and the tube to check their shielding properties. Workshop Video |

| MODERN PHYSICS | 7D30.60 | NUCLEAR PHYSICS |
| --- | --- | --- |
| Particle Detectors |
| Diffusion Cloud Chamber |
|  | This demo requires advance notice to obtain dry ice. Tracks are most impressive if the students are allowed to view individually. The TV works quite well too. |

| MODERN PHYSICS | 7F10.60 | RELATIVITY |
| --- | --- | --- |
| Special Relativity |
| Lorentz Transformation / Time Dilation |
|  | The Mechanical Universe, chapter 42, and the Hewitt film "Relativistic Time Dilation" |